## Slide 1: PADMABHUSHAN DR. VASANTRAODADA PATIL MAHAVIDYALAYA TASGAON DEPARTMENT OF PHYSICS B.Sc-III

## Slide 2: B.Sc. III Paper-XII Digital & Analog circuits & Instrumentation Topic Name:- Logic gate
Prof. Mr. B.S.Harale
Asso.Prof Department of Physics,
PDVP College Tasgaon.

## Slide 3: Introduction: Boolean functions may be practically implemented by using electronic gates. The following points are important to understand. * Electronic gates require a power supply. * Gate INPUTS are driven by voltages having two nominal values, e.g. 0V and 5V representing logic 0 and logic 1 respectively. * The OUTPUT of a gate provides two nominal values of voltage only, e.g. 0V and 5V representing logic 0 and logic 1 respectively. * In general, there is only one output to a logic gate except in some special cases. * There is always a time delay between an input being applied and the output responding.

## Slide 4: Logic gate 1) Basic gate :- OR,AND,NOT 2) gate:- NAND, NOR, Ex-OR, Ex-NOR

## Slide 5: OR Gate :- * The OR gate is a digital logic gate that implements logical disjunction – it behaves according to the adjacent truth table. * A HIGH outputresults if one or both the inputs to the gate are HIGH. * If neither input is high, a LOW output (0) results. * In another sense, the function of OR effectively finds the maximum between two binary digits, just as the complementary AND function finds the minimum.

## Slide 6: Symbolls:-

## Slide 7: AND GATE: *An AND gate is sometimes called the “all or nothing gate”. It has 2 or more input signals. *It produces a 1 output only when all inputs are 1. Otherwise, it produces a 0 output (nothing). *In other words, it produces a 0 output when any input is 0. *An AND gate corresponds to the action of series switches for the input. *The below table shows the four commonly used methods for expressing the AND operation.

## Slide 8: Symbolls:-